## Slide 1
DIGITAL LOGIC DESIGN
(Course Code: ECE 1003)
Module-1:Lecture-2
Number Systems

## Slide 2
Number Systems
CONTENTS
Module-1 (Part-1)
Number systems and conversions
r’s and (r-1)’s compliment
Binary signed and unsigned numbers
Binary arithmetic operations
Weighted and non-weighted binary codes

## Slide 3
Number Systems
CONTENTS
Lecture-2
Conversion of different number systems

## Slide 4
Number Systems
BOOKS
Textbooks
M.Morris Mano, Michael D Ciletti, Digital Design, 5th edition, Pearson Publishers, 2013.
R.P. Jain, “Modern Digital Electronics”, 4th edition, TMH.
References
M.Morris Mano, Charles R. Kime, Tom Martin, Logic and Computer Design Fundamentals, 4th edition, Pearson Publishers.
C. H. Roth and L. L. Kinney, Fundamentals of Logic Design, 5th edition, Cengage Publishers.

## Slide 5
Number Systems
Number Systems

## Slide 6
Number Systems
WORKING OF AN ODOMETER

## Slide 7
Number Systems
NUMBER SYSTEMS
Decimal | Binary | Octal | Hexadecimal
0 | 0000 | 0 | 0
1 | 0001 | 1 | 1
2 | 0010 | 2 | 2
3 | 0011 | 3 | 3
4 | 0100 | 4 | 4
5 | 0101 | 5 | 5
6 | 0110 | 6 | 6
7 | 0111 | 7 | 7
Note:
8 = 23,
Hence each octal number correspond to 3 binary bits

## Slide 8
Number Systems
NUMBER SYSTEMS
Decimal | Binary | Octal | Hexadecimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F
Note:
16 = 24,
Hence each hexadecimal number correspond to 4 binary bits

## Slide 9
Number Systems
NUMBER SYSTEMS
Decimal | Binary | Octal | Hexadecimal
16 | 10000 | 20 | 10
17 | 10001 | 21 | 11
18 | 10010 | 22 | 12
19 | 10011 | 23 | 13
20 | 10100 | 24 | 14
21 | 10101 | 25 | 15
22 | 10110 | 26 | 16
23 | 10111 | 27 | 17
Etc.

## Slide 10
Number Systems
CONVERSION BETWEEN NUMBER BASES
The possibilities:
Decimal
Octal
Binary
Hexadecimal

## Slide 11
Number Systems
CONVERSION FROM DECIMAL TO ANOTHER BASE
Convert an Integer from Decimal to Another Base
For each digit position:
Divide decimal number by the base (e.g. 2)
The remainder is the lowest-order digit
Repeat first two steps until no divisor remains.
Convert a fraction from Decimal to Another Base
For each digit position:
Multiply decimal number by the base (e.g. 2)
The integer is the highest-order digit
Repeat first two steps until fraction becomes zero.
Decimal
Octal
Binary
Hexadecimal

## Slide 12
Number Systems
CONVERSION FROM DECIMAL TO BINARY
Decimal
Octal
Binary
Hexadecimal

## Slide 13
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM DECIMAL TO BINARY
Convert an Integer from Decimal to Binary
Example for (13)10:
Integer
Quotient
13/2 = 6 + 1 a0 = 1
6/2 = 3 + 0 a1 = 0
3/2 = 1 + 1 a2 = 1
1/2 = 0 + 1 a3 = 1
Remainder
Coefficient
(13)10 = (a3 a2 a1 a0)2 = (1101)2

## Slide 14
Number Systems
CONVERSION FROM DECIMAL TO BINARY
Convert a fraction from Decimal to Binary
Example for (0.625)10 :
Integer
Fraction
Coefficient
0.625 x 2 = 1 + 0.25 a-1 = 1
0.250 x 2 = 0 + 0.50 a-2 = 0
0.500 x 2 = 1 + 0 a-3 = 1
(0.625)10 = (0.a-1 a-2 a-3 )2 = (0.101)2

## Slide 15
Number Systems
CONVERSION FROM DECIMAL TO BINARY
Example: Convert (23.6)10 to binary :
(23.6)10 = (10111.10011)2 (fractional part truncated at 5 bits)

## Slide 16
Number Systems
CONVERSION FROM DECIMAL TO BINARY
Example:
(125)10 = (1111101)2
Trick:
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1

## Slide 17
Number Systems
CONVERSION FROM DECIMAL TO OCTAL
Decimal
Octal
Binary
Hexadecimal

## Slide 18
Number Systems
CONVERSION FROM DECIMAL TO OCTAL
Convert an Integer from Decimal to Octal
Example for (175)10:
Integer
Quotient
Remainder
Coefficient
175/8 = 21 + 7 a0 = 7
21/8 = 2 + 5 a1 = 5
2/8 = 0 + 2 a2 = 2
(175)10 = (a2 a1 a0)8 = (257)8

## Slide 19
Number Systems
CONVERSION FROM DECIMAL TO OCTAL
Convert a fraction from Decimal to Octal
Example for (0.3125)10 :
Integer
Fraction
Coefficient
0.3125 x 8 = 2 + 0.5 a-1 = 2
0.5000 x 8 = 4 + 0 a-2 = 4
(0.3125)10 = (0.24)8

## Slide 20
Number Systems
Example:
(1234)10 = (2322)8
CONVERSION FROM DECIMAL TO OCTAL

## Slide 21
Number Systems
CONVERSION FROM DECIMAL TO HEXADECIMAL
Decimal
Octal
Binary
Hexadecimal

## Slide 22
Number Systems
CONVERSION FROM DECIMAL TO HEXADECIMAL
Convert an Integer from Decimal to Hexadecimal
Example for (257)10:
Integer
Quotient
Remainder
Coefficient
257/16 = 16 + 1 a0 = 1
16/16 = 1 + 0 a1 = 0
1/16 = 0 + 1 a2 = 1
(257)10 = (a2 a1 a0)16 = (101)16

## Slide 23
Number Systems
Convert a fraction from Decimal to Hexadecimal
Example for (0.1275)10 :
Integer
Fraction
Coefficient
0.1275 x 16 = 2 + 0.04 a-1 = 2
0.04 x 16 = 0 + 0.64 a-2 = 0
0.64 x 16 = 10 + 0.24 a-3 = A
- - - - - - - - - - - - - - - - -
(0.1275)10 = (0.20A)16
CONVERSION FROM DECIMAL TO HEXADECIMAL

## Slide 24
Number Systems
Example:
(1234)10 = (4D2)16
CONVERSION FROM DECIMAL TO HEXADECIMAL

## Slide 25
Number Systems
CONVERSION FROM ANY BASE TO DECIMAL
Technique:
Multiply each bit by bn, where n is the “weight” of the bit and b is the base.
The weight is the position of the bit, starting from 0 on the right
Add the results
Decimal
Octal
Binary
Hexadecimal

## Slide 26
Number Systems
CONVERSION FROM BINARY TO DECIMAL
Decimal
Octal
Binary
Hexadecimal

## Slide 27
Number Systems
Example: (101011)2 = (N)10
(101011)2 = (43)10
CONVERSION FROM BINARY TO DECIMAL
1010112 => 1 x 20 = 1 1 x 21 = 2 0 x 22 = 0 1 x 23 = 8 0 x 24 = 0 1 x 25 = 32 4310

## Slide 28
Number Systems
Example: (10.1011)2 = (N)10
(10.1011)2 = (2.6875)10
CONVERSION FROM BINARY TO DECIMAL
10.10112 => 1 x 2-4 = 0.0625 1 x 2-3 = 0.125 0 x 2-2 = 0.0 1 x 2-1 = 0.5 0 x 20 = 0 1 x 21 = 2 2.687510

## Slide 29
Number Systems
CONVERSION FROM OCTAL TO DECIMAL
Decimal
Octal
Binary
Hexadecimal

## Slide 30
Number Systems
Example: (724)8 = (N)10
(724)8 = (468)10
CONVERSION FROM OCTAL TO DECIMAL

## Slide 31
Number Systems
CONVERSION FROM HEXADECIMAL TO DECIMAL
Decimal
Octal
Binary
Hexadecimal

## Slide 32
Number Systems
Example: (ABC)16 = (N)10
(ABC)16 = (2748)10
CONVERSION FROM HEXADECIMAL TO DECIMAL

## Slide 33
Number Systems
Fill the table:
ASSIGNMENT QUESTION

## Slide 34
Please follow the instructions of the government and stay safe
Number Systems