## Slide 1
DIGITAL LOGIC DESIGN
(Course Code: ECE 1003)
Dr. Subhasish Mahapatra
Sr. Assistant Professor
School of Electronics Engineering (SENSE)
VIT-AP University
E-Mail: subhasish.m@vitap.ac.in
Module-1:Lecture-3
Number Systems

## Slide 2
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONTENTS
Module-1 (Part-1)
Number systems and conversions
Binary arithmetic operations
r’s and (r-1)’s compliment
Binary signed and unsigned numbers
Weighted and non-weighted binary codes

## Slide 3
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONTENTS
Lecture-3
Conversion of different number systems (cont…)
Binary Arithmetic

## Slide 4
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
BOOKS
Textbooks
M.Morris Mano, Michael D Ciletti, Digital Design, 5th edition, Pearson Publishers, 2013.
R.P. Jain, “Modern Digital Electronics”, 4th edition, TMH.
References
M.Morris Mano, Charles R. Kime, Tom Martin, Logic and Computer Design Fundamentals, 4th edition, Pearson Publishers.
C. H. Roth and L. L. Kinney, Fundamentals of Logic Design, 5th edition, Cengage Publishers.

## Slide 5
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
Number Systems

## Slide 6
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION BETWEEN NUMBER BASES
The possibilities:
Decimal
Octal
Binary
Hexadecimal

## Slide 7
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM BINARY TO OCTAL
Decimal
Octal
Binary
Hexadecimal

## Slide 8
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM BINARY TO OCTAL
Technique:
Group bits in threes, starting on right for integer part and from left for fractional part.
Ignore leading zeros and add zeros after decimal if necessary, to form group of three bits.
Convert to octal digits
Example: (1011010111)2 = (N)8
(1011010111)2 = (1327)8

## Slide 9
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM BINARY TO OCTAL
Example: (1010111000.0101)2 = (N)8
(1010111000.0101)2 = (1270.24)8
1 010 111 000 . 010 100
1 2 7 0 . 2 4

## Slide 10
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM BINARY TO HEXADECIMAL
Decimal
Octal
Binary
Hexadecimal

## Slide 11
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM BINARY TO HEXADECIMAL
Technique:
Group bits in fours, starting on right for integer part and from left for fractional part.
Ignore leading zeros and add zeros after decimal if necessary, to form group of four bits.
Convert to hexadecimal digits
Example: (1010111011)2 = (N)16
(1010111011)2 = (2BB)16

## Slide 12
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM BINARY TO OCTAL
Example: (1010111000.0101)2 = (N)16
(1010111000.0101)2 = (2B8.5)16
0010 1011 1000 . 0101
2 B 8 . 5

## Slide 13
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM OCTAL TO BINARY
Decimal
Octal
Binary
Hexadecimal

## Slide 14
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM OCTAL TO BINARY
Technique:
Convert each octal digit to a 3-bit equivalent binary representation
Example: (705)8 = (N)2
(705)8 = (111000101)2

## Slide 15
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM OCTAL TO BINARY
Example: (1472.16)8 = (N)2
(1472.16)8 = (1100111010.00111)2
1 100 111 010 . 001 110
1 4 7 2 . 1 6

## Slide 16
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM OCTAL TO HEXADECIMAL
Decimal
Octal
Binary
Hexadecimal

## Slide 17
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
Technique:
Use binary as an intermediary
Example: (1472.16)8 = (N)16
(1472.16)8 = (33A.38)16
1 100 111 010 . 001 110
1 4 7 2 . 1 6
001 100 111 010 . 001 11000
3 3 A . 3 8
CONVERSION FROM OCTAL TO HEXADECIMAL

## Slide 18
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM HEXADECIMAL TO BINARY
Decimal
Octal
Binary
Hexadecimal

## Slide 19
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM HEXADECIMAL TO BINARY
Technique:
Convert each hexadecimal digit to a 4-bit equivalent binary representation
Example: (10AF)16 = (N)2
(10AF)16 = (1000010101111)2

## Slide 20
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM HEXADECIMAL TO BINARY
Example: (A5BF.0C)16 = (N)2
(A5BF.0C)16 = (1010010110111111.000011)2
A 5 B F . 0 C
1010 0101 1011 1111 . 0000 1100

## Slide 21
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
CONVERSION FROM HEXADECIMAL TO OCTAL
Decimal
Octal
Binary
Hexadecimal

## Slide 22
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
Technique:
Use binary as an intermediary
Example: (A5BF.0C)16 = (N)8
(A5BF.0C)16 = (122677.03)8
1 2 2 6 7 7 . 0 3
CONVERSION FROM HEXADECIMAL TO OCTAL
A 5 B F . 0 C
1010 0101 1011 1111 . 0000 1100
001010 0101 1011 1111 . 0000 1100

## Slide 23
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
ASSIGNMENT QUESTION
Fill the table:

## Slide 24
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
Binary Arithmetic

## Slide 25
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
BINARY ADDITION
Two 1-bit values:

## Slide 26
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
BINARY ADDITION
Two n-bit values:
Add individual bits
Propagate carries
Example:
1 1 1 1 0 1
+ 1 0 1 1 1
---------------------
0
1
0
1
1
1
1
1
1
1
1
0
0
carries
6 1
+ 2 3
----------
4
8

## Slide 27
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
BINARY ADDITION
Two n-bit values:
Add individual bits
Propagate carries
Example:

## Slide 28
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
BINARY SUBTRACTION
Two 1-bit values:
With Borrow 1

## Slide 29
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
Two n-bit values:
Subtract individual bits with borrow if necessary
Example:
1 1 1 1 0 1
+ 1 0 1 1 1
---------------------
0
10
1
0
1
0
0
0
1
Borrows
6 1
- 2 3
----------
8
3
BINARY SUBTRACTION
10
10- decimal value 2

## Slide 30
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
BINARY MULTIPLICATION
Two 1-bit values:

## Slide 31
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
Example:
1 0 1 1 1
X 1 0 1 0
-----------------------
0 0 0 0 0
1 0 1 1 1
0 0 0 0 0
1 0 1 1 1
-----------------------
1 1 1 0 0 1 1 0
2 3
X 1 0
----------
0
3
2
BINARY MULTIPLICATION

## Slide 32
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Number Systems
Add: (1000111)2 + (1110)2
Subtract: (1110000)2 – (1111)2
Multiply: (101)2 x (10101)2
ASSIGNMENT QUESTIONS

## Slide 33
Dr. Subhasish Mahapatra
Sr. Assistant Professor, SENSE
Please follow the instructions of the government and stay safe
Number Systems